## Slide 1: Autonomous Wheelchair using Structured Light
Michael Hodgson
John Charlesworth

## Slide 2: Contents
Aims
Structured Light
Original 2D Investigation
3D Point Cloud
  Point Cloud Library
  Voxel Grid
  Floor Removal
  Clear Direction
  Pathfinding
Demo
Questions

## Slide 3: Aim
To provide obstacle detection and avoidance using structured light
+
= ?

## Slide 4: Previous Work Example
Autonomous Navigation Using a Real-Time 3D Point Cloud. Whitty, M. et al. Australasian Conference on Robotics and Automation. 2010
  Complex system using multiple robots with laser scanners, IMU and SLAM techniques
  Uses occupancy grid and path finding

## Slide 5: Structured Light (Kinect)
We are using the Microsoft Kinect
Structured light 3D sensor
Works by:
  Projecting a pattern (IR laser grid)
  Observing how this is distorted when viewed from another view point (IR CMOS sensor)
Laser
IR Sensor

## Slide 6: Original 2D Investigation
Data captured by screenshot, then microsoft SDK and finally openNI viewer
Transferred to MATLAB for processing:
  Floor removal
  Depth thresholding
Raw depth data
Floor removed
Depth thresholded

## Slide 7: 3D Point Cloud
The structured light sensor generates a point cloud

## Slide 8: 3D Point Cloud – Method Overview
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 9: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 10: 3D Point Cloud – Point Cloud Library
The Point Cloud Library (PCL) was used in this project
The PCL is a C++ library for manipulating point clouds
It provides access to a wide range of functions in areas such as filtering, segmentation and visualisation.
http://pointclouds.org/

## Slide 11: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 12: 3D Point Cloud - Voxel Grid Downsampling
Reasons we downsampled in a uniform grid:
  Speed (too many points)
  Larger point density close to Kinect
PCL’s built in filter creates a 3D voxel grid over the point cloud data
  Downsamples using centroids of all points in voxel[1]
[1] http://docs.pointclouds.org/trunk/classpcl_1_1_voxel_grid.html#_details

## Slide 13: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 14: 3D Point Cloud – Floor Detection
Different methods were used to detect the floor
Based on comparison with planes
  First Method: manually sweep through planes (slow)
  Second Method: manually remove ceiling and use RANSAC algorithm
Notes: Top image brute force, bottom RANSAC

## Slide 15: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 16: 3D Point Cloud – Clear Direction
Calculation of clear directions
Method:
  Box is swept across scene
  Floor points and obstacle points within box counted
  Boxes with floor points above a threshold and obstacle points below a threshold are marked as clear and displayed
  Box length variable

## Slide 17: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 18: 3D Point Cloud – Occupancy Map
A 2D Occupancy map was constructed
Method:
  Floor captured, dilated and marked as passable
  Obstacle points captured, dilated and marked as impassable
Dilation to account for wheelchair width

## Slide 19: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 20: 3D Point Cloud - Pathfinding
Using occupancy map
Pathfinding done using the A* algorithm
Single start point, multiple radial finish points
Finish point distance variable

## Slide 21: For Your Information – A* (A Star) Search Algorithm
Faster extension of Dijkstra's algorithm
Space represented as 2D array with each cell either passable or impassable
Uses a distance-plus-cost function to determine which nodes to search next:
  Function of cost from start cell to current cell
  Plus estimated distance from current cell to finish
http://en.wikipedia.org/wiki/File:Astar_progress_animation.gif

## Slide 22: Demonstration

## Slide 23: Technical Summary
Detection range: up to 5m (reliable)
Configurable detection length: 2 – 5m
Lanes sweep across 30o field of view in 20 steps
Average frame rate:
  Without pathfinding: ~4 fps
  With pathfinding: ~0.5 fps

## Slide 24: Summary
Point Cloud Extracted
Clear Directions Selected
Pathfinding Implemented
Further Work:
  SLAM integration
  Interfacing with a robot
  GPS integration

## Slide 25: Source Code
We have used a Git repository to store our source code
  Homepage: https://github.com/michaelwh/kinect-wheelchair
  Download the latest code, test images and test/development log (zip): https://github.com/michaelwh/kinect-wheelchair/zipball/master

## Slide 26: Testing and Development: Further Info
We have kept an online log of the development of this project with plenty of testing detail
  Please see it at https://docs.google.com/document/d/1Mtvac63xoO_FK9xakpljxqftgFCKUsIqAUdaZ14av8U/edit
  It is also in the git repository

## Slide 27: Resources Used
http://www.araa.asn.au/acra/acra2010/papers/pap151s1-file1.pdf
  Talks about navigating using an occupancy grid and point cloud
http://www.ipb.uni-bonn.de/uploads/tx_ikgpublication/Plane_Detection_in_Point_Cloud_Data.pdf
  A couple of plane detection algorithms for point clouds
Point Cloud Library (PCL) http://pointclouds.org/
  We use this for a lot of things in our algorithms including voxel grid downsampling, plane detection using RANSAC and visualisation of point cloud data - this is an excellent library with a huge number of features, although it is still quite rough around the edges, inconsistent and difficult to use at times.
http://svn.pointclouds.org/pcl/trunk/visualization/tools/openni_viewer.cpp
  Our implementation has been based on the framework provided by this code which extracts point cloud data and image data from a Kinect and displays it on screen
http://code.activestate.com/recipes/577457-a-star-shortest-path-algorithm/
  The code for the A* pathfinding algorithm used was taken from here.

## Slide 28: Any Questions?