## Slide 1: Autonomous Wheelchair using Structured Light
Michael Hodgson
John Charlesworth

## Slide 2: Contents
Aims
Structured Light
Original 2D Investigation
3D Point Cloud
  Point Cloud Library
  Voxel Grid
  Floor Removal
  Clear Direction
  Pathfinding
Demo
Questions

## Slide 3: Aims
To provide obstacle detection and avoidance using structured light

## Slide 4: Structured Light (Kinect)
We are using the Microsoft Kinect
Structured light 3D sensor
Works by:
  Projecting a pattern (IR laser grid)
  Observing how this is distorted when viewed from another view point (IR CMOS sensor)
Laser
IR Sensor

## Slide 5: Original 2D Investigation
Data captured by screenshot, then microsoft SDK and finally openNI viewer
Transferred to MATLAB for processing:
  Floor removal
  Depth thresholding
Raw depth data
Floor removed
Depth thresholded

## Slide 6: 3D Point Cloud
The structured light sensor generates a point cloud

## Slide 7: 3D Point Cloud – Method Overview
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 8: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 9: 3D Point Cloud – Point Cloud Library
The Point Cloud Library (PCL) was used in this project
The PCL is a C++ library for manipulating point clouds
It provides access to a wide range of functions in areas such as filtering, segmentation and visualisation.
http://pointclouds.org/

## Slide 10: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 11: 3D Point Cloud - Voxel Grid Downsampling
Reasons we downsampled in a uniform grid:
  Speed (too many points)
  Larger point density close to Kinect
PCL’s built in filter creates a 3D voxel grid over the point cloud data
  Downsamples using centroids of all points in voxel[1]
[1] http://docs.pointclouds.org/trunk/classpcl_1_1_voxel_grid.html#_details

## Slide 12: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 13: 3D Point Cloud – Floor Detection
Different methods were used to detect the floor
Based on comparison with planes
  First Method: manually sweep through planes (slow)
  Second Method: manually remove ceiling and use RANSAC algorithm
Notes: Top image brute force, bottom RANSAC

## Slide 14: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 15: 3D Point Cloud – Clear Direction
Calculation of clear directions
Method:
  Box is swept across scene
  Floor points and obstacle points within box counted
  Boxes with floor points above a threshold and obstacle points below a threshold are marked as clear and displayed
  Box length variable

## Slide 16: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 17: 3D Point Cloud – Occupancy Map
A 2D Occupancy map was constructed
Method:
  Floor captured, dilated and marked as passable
  Obstacle points captured, dilated and marked as impassable
Dilation to account for wheelchair width

## Slide 18: 3D Point Cloud
Point Cloud
Voxel
Floor Detection
Occupancy Map
Clear Direction
Pathfinding

## Slide 19: 3D Point Cloud - Pathfinding
Using occupancy map
Pathfinding done using the A* algorithm
Single start point, multiple radial finish points
Finish point distance variable

## Slide 20: For Your Information – A* (A Star) Search Algorithm
Faster extension of Dijkstra's algorithm
Space represented as 2D array with each cell either passable or impassable
Uses a distance-plus-cost function to determine which nodes to search next:
  Function of cost from start cell to current cell
  Plus estimated distance from current cell to finish
http://en.wikipedia.org/wiki/File:Astar_progress_animation.gif

## Slide 21: Demonstration

## Slide 22: Technical Summary
Detection range: up to 5m (reliable)
Configurable detection length: 2 – 5m
Lanes sweep across 30o field of view in 20 steps
Average frame rate:
  Without pathfinding: ~4 fps
  With pathfinding: ~0.5 fps

## Slide 23: Summary
Point Cloud Extracted
Clear Directions Selected
Pathfinding Implemented
Further Work:
  SLAM integration
  Interfacing with a robot
  GPS integration

## Slide 24: Any Questions?