## Slide 1: Autonomous Wheelchair using Structured Light
Michael Hodgson,
John Charlesworth,
Adham Beyki and
Mahdi Naddaf

## Slide 2: Contents
Aims
Structured Light
Original 2D Investigation
3D Point Cloud
  Point Cloud Library
  Voxel Grid
  Floor Removal
  Clear Direction
  Pathfinding
  Other Work
Demo
Questions

## Slide 3: Aims
To provide obstacle detection and avoidance using structured light

## Slide 4: Structured Light (Kinect)
We are using the Microsoft Kinect
Structured light 3D sensor
Works by:
  Projecting a pattern (IR laser grid)
  Observing how this is distorted when viewed from another view point (IR CMOS sensor)
Laser
IR Sensor

## Slide 5: Original 2D Investigation
Data captured by screenshot, then microsoft SDK and finally openNI viewer
Transferred to MATLAB for processing:
  Floor removal
  Depth thresholding
Raw depth data
Floor removed
Depth thresholded

## Slide 6: 3D Point Cloud
The structured light sensor generates a point cloud

## Slide 7: 3D Point Cloud – Point Cloud Library
The Point Cloud Library (PCL) was used in this project
The PCL is a C++ library for manipulating point clouds
It provides access to a wide range of functions in areas such as filtering, segmentation and visualisation.
http://pointclouds.org/

## Slide 8: 3D Point Cloud – Voxel Grid

## Slide 9: 3D Point Cloud – Floor Detection
Different methods were used to detect the floor
Based on comparison with planes
  First Method: manually sweep through planes (slow)
  Second Method: manually remove ceiling and use RANSAC algorithm
Notes: Top image brute force, bottom RANSAC

## Slide 10: For Your Information - RANSAC

## Slide 11: 3D Point Cloud – Clear Direction
Calculation of clear directions
Method:
  Box is swept across scene
  Floor points and obstacle points within box counted
  Boxes with floor points above a threshold and obstacle points below a threshold are marked as clear and displayed
  Box length variable

## Slide 12: 3D Point Cloud – Occupancy Map
A 2D Occupancy map was constructed
Method:
  Floor captured, dilated and marked as passable
  Obstacle points captured, dilated and marked as impassable
Dilation to account for wheelchair width

## Slide 13: 3D Point Cloud - Pathfinding
Using occupancy map
Pathfinding done using the A* algorithm
Single start point, multiple radial finish points
Finish point distance variable

## Slide 14: For Your Information – A* (A Star) Pathfinding Algorithm

## Slide 15: 3D Point Clouds – Other Work

## Slide 16: Demonstration

## Slide 17: Any Questions?